Interactive 3D Rapid-Prototyping Models
---
Carlo H. Séquin
 U.C. Berkeley, EECS, CS Division
Dissection Geometries
Fabrication Issues
A Simple Introduction to Polyhedral Dissections
Interlocking Cubic Burr Puzzle
Problem Statement:
Here is a picture of a neat cube-dissection puzzle. We would like to have one like it,
-- but at a much bigger scale (say, scaled up by a factor of 8 or 10)!
Find a design that can be built at this larger scale in an economical way
with a layered manufacturing process.
Hamiltonian dissections of Platonic Solids: The cutting surface is formed by a line sweeping
from the centroid of the solid along a Hamiltonian cycle on the polyhedron edges.
Making Truly Interactive 3D Models
Not just virtual displays that can be twiddled with a mouse.
But tangible 3D models that can be physically manipulated.
Dissection puzzles are excellent tutorial examples:
Helicoidal Dissections
Solution: Use a grid / frame approach to outline each unit cube:
Problem Statement:
Design a two- or three-piece geometrical puzzle in which a simple shape
partitions into all congruent parts via a helical screw motion.
Instructional / Educational Value
of 3D Dissection Puzzles
Possible cubelet designs: (a) cross section through a hollow cube shell; (b) Leonardo-style
cube frame; (c) cross section through this cube frame with support structure
(dark vertical lines); (d) final cubelet frame design with beveled edges.
 Used in course on Solid Modeling & Rapid Prototyping:
  The design of the 3D puzzle geometry
requires spatial visualization skills.
The design of the physical artifacts
requires attention to tolerances
and to materials properties.
A first approach: Define one or more helicoidal cutting planes around the z-axis
and use those to cut up a shape with proper rotational symmetry around this axis.
Tangible Models
Provide relevant feedback on whether parts fit together
     and have the right amount of resistance to movements:
so that they don’ t fall apart by themselves;
so that they don’t stick too tightly together.
Success is judged by manipulating the model.
(a) One frame part as it comes out of the FDM machine; (b) another part after removal of the support structure; (c) the whole 4x4x4 burr puzzle assembled.
A second approach: Define the extrusion of a suitable cross section and its complement;
Helically twist the whole configuration around the z-axis.
      Tolerances ! Dissecting All of 3D Space
Multi-hand Dissections
Play with the models !
In this ring of 5 tiles at least 3 tiles have to be moved simultaneously in different directions
in order to take this puzzle apart.
Too tight ??
Isohedral helicoidal tiles (Matthias Goerner)

---
Bending and Twisting
Optimizing the Torus Eversion Process
Shape Optimization of Toroidal Sweeps
The Rotation Minimizing Sweep completely defines the relative orientations of the two endpoints of a 3D space curve.
For non-planar closed space curves, the ends may not match up. We can force a match by introducing additional twist along the sweep.
When we change the shape of the space curve, the amount of needed twist may change.
Avik Das
Advisor: Carlo H. Séquin
EECS
Smooth Transformations
Regular homotopy:Smooth transformation from one surface to another without introducing sharp creases or tears.
Want to visualize such transformations without specifying intermediate states, achieved by an optimization process over some energy functional.
Turning a torus inside out is a regular homotopy.
Want to visualize this process proceeding spontaneously from some halfway point.
A planar figure-8 with no twist, but more bending than a circle
Unfolding the figure-8
Same regular homotopy class
Fully unfolded into a circle with 360° of accumulated twist from the unfolding
Torus Eversion
Chéritat provides a visualization of torus eversion
He creates a short, everted tube section between two Klein-bottle mouths. These travel in opposite directions around toroidal loop and recombine.
Energy Functionals
Torus represented by a circular cross-section swept along a time-varying space curve.
Evaluate the quality of a configuration based on:
Bending: Compute angle between two struts and take deviation from collinearity
Twisting: Using rotation minimizing frames, add necessary twist to meet given orientation constraints. For example, the final torus should have matching endpoints and no twist.
Future Work
Would we find a more elegant path if the system had more degrees of freedom?
Non-uniform twist, varying cross sections. Best path may not be expressible as a sweep.
Fully gridded parameterization of surface
Requires many control points, so many parameters over which to optimize
Optimization by Gradient Descent
Vary the coordinates of each control point (parameters), revert change if energy does not decrease
Iterate, then stop when no decrease possible
Susceptible to local minima in energy functional
Optimized sphere eversion has been achieved by starting at a halfway point and allowing an energy functional to guide the rest of the process. Can we do the same for a torus with the “(##)” halfway point below?
A highly twisted and bent curve unfolds into a circle with no twist, using gradient descent.
(##)
Integrate these over entire surface area
With a general enough energy functional, hope to automatically find unknown regular homotopy moves between surfaces in the same regular homotopy class (e.g. parameter swap of tori).
Klein-bottle mouths
The stripe on the right arm is shown here. If an ant were to walk on the stripe, it would end up rotating about 170°.
The regular homotopy from a torus to the (##) halfway point incurs 360° of twist, i.e. 180° in each branch. By penalizing twist, can we encourage the shape to return to a regular torus?
We model the two arms as separate space curves, connected by end caps (not shown). The endpoints are constraint to have matching orientation. When twist is penalized sufficiently, the curve takes on a shape that provides 90% of the orientation change based only on the sweep path.
This is hardly closer to the desired torus! Still a halfway point; we need to deliberately break the symmetry.
Straightening out one arm: By forcing the green arm to straighten and the end caps to come closer together, the red arm is forced to absorb all 360° of twist. It does so by forming a loop that rotates 180° through space until it takes on a toroidal shape.
Collapsing the straight arm: Finally, the green arm is shortened until it completely collapses and only the red torus remains.
Bending calculated as rate of change of surface normal.
Twisting calculated based on skewed quadrilaterals and measuring angles between neighboring struts.